## Slide 1: Prototype 1 IoT4Lunch
Temperature Only

## Slide 2
Teensy 1
RaspberryPi
Collect Temperature
Set Thresholds
Send Bluetooth to Raspberry Pi
Received Data from Teensy
*Set Threshold
import time
# Replace tempC with the actual temperature value you want to check
tempC = 6.5 # Example temperature value
if tempC < 4.0:
print(f"Temperature: {tempC}°C - [Safe]")
time.sleep(10) # Sleep for 10 seconds
elif 4.0 <= tempC <= 8.0:
print(f"Temperature: {tempC}°C - [Caution]")
time.sleep(10) # Sleep for 10 seconds
else:
print(f"Temperature: {tempC}°C - [Warning]")
time.sleep(10) # Sleep for 10 seconds

## Slide 3
Teensy 2
Receive data from AWS
If msg.payload contains safe led 1 high
Else if msg.payload contains caution
led 2 high
Else msg.payload contains warning
led 3 high
buzzertone(1000)
delay 1 (Second)
buzztone off

## Slide 4: Actuator Led with Buzzer

## Slide 5: Actuator Led with Buzzer
//Define Pins
const int led1 = 1; //Red LED
const int led2 = 2; //Yellow LED
const int led3 = 3; //Green LED
const int buzzer = 4; //Buzzer
void setup() {
Serial.begin(9600); // Delivering Data from Bluetooth
Serial1.begin(9600); // Incoming data from Bluetooth
pinMode(led1, OUTPUT);
pinMode(led2, OUTPUT);
pinMode(led3, OUTPUT);
pinMode(buzzer, OUTPUT);
}
void loop() {
// Check if there is incoming serial data
if (Serial1.available() > 0)
{
String str = Serial1.readString().substring(0); // Read the incoming data as a String
// Print received data for debugging
Serial.println("Received data: " + str);
// Check if the received data contains "warning" (case-insensitive)
if (str.indexOf("Warning") != -1)
{
// Turn on the LED
digitalWrite(led1, HIGH);
Serial.println("Warning");
tone(buzzer, 100);
delay(1000); // Keep the LED on for 1 second
noTone(buzzer);
digitalWrite(led1, LOW); // Turn off the LED
}
}
}

## Slide 6: Receiving Notifications on Phone
What is AWS IoT Core?

## Slide 7: 8 Dot Matrix
https://electropeak.com/learn/using-8x8-dot-matrix-led-arduino-cascade-connection/

## Slide 8: LED Rotary Encoder

## Slide 9: Ideas
How to implement an led bar counter for IOT device.
Change polling rate.

## Slide 10: Tri-sensor
X = 450 – 550 | Safe
Y = safe 600 , under 600 unsafe, 500 flat

## Slide 11: Logic
IOT Device 1 : Temperature Sensor, XYZ Sensor, Bluetooth
Modes
  Initialized – No Data
  Mode 1 – Temperature And Motion
  Mode 2 – Temperature
  Mode 3 – Motion
Modes are set by IOT Device 2.
IOT Device 2 : 6 LEDs (4 in a Row, 2 Separate), Rotary Encoder, LED Button.
  4 in a Row :
    Red is Initialized
    Green is – Temperature and Motion
    Orange is Temperature
    Yellow is Motion
  2 Separate :
    Green = In Mode
    Red = Not in Current Mode
  Rotary Encoder
    Counter = 1-4. 1 is off, 2 is mode 1, 3 is mode 2, 4 is mode 3.
    Switch = Ok signal to send signal to IOT Device 2 to change mode.
IOT Device 3: 1x Buzzer, 1x Traffic Light, 1x Yellow, 1x Red
  Buzzer works with Traffic Light. On red a sound byte will be played.
  Green means it is within temperature
  Yellow means its reaching a certain temperature
  Red is a Warning.
  2nd Red Light indicates that if the box is tipped over
  Yellow cautions its leaning.

## Slide 12: Rotary Encoder Redesign

## Slide 13: IoT Temperature Device
Wiring diagram

## Slide 14: IOT Device 1.
Remember to use the right resistor.

## Slide 15: Temp + LCD working
Can only use first row due to limited power
If Temp is Below 4 it will display OK
If it is equal to 4 and less than 8 displays !
If it is more than 9 it will display !!!

## Slide 16: Mode Testing
Completed

## Slide 17: Rotatory Encoder